## Slide 1
NAS-PINN k-Skip Framework
for Thermal Quenching Simulation
Solving the transient heat equation for aluminium quenching using
Physics-Informed Neural Networks with Neural Architecture Search
Mortensen D. et al. (2026) Int. J. Adv. Manuf. Technol. doi:10.1007/s00170-026-17515-w | Wang & Zhong (2023) arXiv:2305.10127
March 2026

## Slide 2
Motivation & Problem Statement
Why reduce FEM calls for quenching?
FEM Limitations
• High computational cost for 3D transient simulations
• Each FEM step requires mesh assembly and linear solve
• 20 time-steps at Δt=1.5 s → sequential bottleneck
• Repeated evaluations needed for design optimisation
• Scaling to large automotive subframes is prohibitive
PINN + NAS Advantages
• Mesh-free: collocated PDE residual evaluation
• Once trained, inference is near-instantaneous
• k-Skip reduces FEM supervision calls by up to 5×
• NAS automatically finds optimal architecture
• Generalises across 2D and 3D geometries
• IC-consistent output layer guarantees exact ICs
Goal: maintain L2 < 3% while reducing FEM calls by up to 5×

## Slide 3
Physical Problem
Transient heat equation — aluminium quenching
Governing Equation
ρcₚ ∂T/∂t = ∇·(k∇T) + Q
BC: −k ∂T/∂n = h(T − Tᵢᵣ), h = 5000 W/m²K
IC: T(x, 0) = 500 °C Tᵢᵣ = 20 °C
Problem Parameters
• Material: Aluminium alloy (A356)
• T_initial = 500 °C, T_water = 20 °C, t_total = 30 s
• FEM discretisation: Δt_FEM = 1.5 s → 20 time steps
• Mortensen D. et al. (2026) Int. J. Adv. Manuf. Technol. doi:10.1007/s00170-026-17515-w
Domains Tested
2D:
Rectangle, Circle, L-shape
3D:
Rectangular box, Cylinder,
Stacked, L-shape (3D)
FEM steps: 20 @ Δt=1.5 s
k-skip windows per k:
k=1
20 wins
k=2
10 wins
k=3
7 wins
k=4
5 wins
k=5
4 wins
Quenching process: 500 °C → water at 20 °C — rapid thermal gradient drives distortion

## Slide 4
Methodology Overview
k-Skip Multi-Step Window Prediction (MSWP) pipeline
Methodology Overview
k-Skip Multi-Step Window Prediction (MSWP) pipeline
FEM Reference (t=0,k,2k,...)
IC-Consistent PINN Output θ̂ = θ_ic + τ·Nθ
Fourier Embedding γ(v)=[sin,cos]
Self-Adaptive Loss Weights λ=softplus(w)
NAS Optimiser Bayes/NSGA
→
→
→
→
k-Skip Window
Window = k × 1.5 s k ∈ {1,2,3,4,5} FEM calls ↓
Training Losses
L = λ_pde·L_pde + λ_bc·L_bc + λ_end·L_end
Epochs
Phase 1: 800 ep Phase 2: 1500 ep (NSGA-II/III retrain)
Search Space
Depth, width, activation, skip connections
Step 1
Step 2
Step 3
Step 4
Step 5
k-Skip: PINN predicts T over k FEM steps — reduces supervision cost up to 5×

## Slide 5
k-Skip Framework
FEM call reduction via temporal window skipping
k-Skip Framework
FEM call reduction via temporal window skipping
k-Skip Parameters
k
Δt_window (s)
FEM Windows
FEM Calls↓
Speedup
1
1.5
20
1.0×
baseline
2
3.0
10
2.0×
↑ fast
3
4.5
7
2.9×
↑↑ fast
4
6.0
5
4.0×
↑↑↑ fast
5
7.5
4
5.0×
↑↑↑↑ max
IC-Consistent Output Layer
θ̂(x,τ) = θ_ic(x) + τ · Nθ(x, τ, θ_ic)
τ ∈ [0,1] — normalised time within window
Loss Function
L = λ_pde · L_pde + λ_bc · L_bc + λ_end · L_end
λᵢ = softplus(wᵢ) — learned jointly with network
η_model = 1×10⁻³, η_λ = 1×10⁻⁴
Fourier Feature Embedding
γ(v) = [sin(2πBv), cos(2πBv)]
F=64 frequencies, σ=1.0 (2D), σ=1.5 (3D)
Larger k = fewer FEM calls; IC-consistent PINN exactly satisfies initial condition every window

## Slide 6
PINN Architecture
IC-consistent output, Fourier embedding, self-adaptive weights
PINN Architecture
Input Layer
x, y (,z), t + Fourier embedding γ(v)
Hidden Layers (NAS-optimised)
Depth: 2–6 Width: 16–256 Act: tanh/swish Skip connections
IC-Consistent Output
θ̂ = θ_ic + τ·Nθ Exact IC at τ=0 Smooth BC satisfaction
Temperature Prediction
T(x,y,z,t) in °C L2 < 3% (2D) L2 < 7% (3D)
→
→
→
Fourier Features
• γ(v) = [sin(2πBv), cos(2πBv)]
• B ∼ N(0,σ²) fixed random matrix
• F = 64 frequency pairs
• σ = 1.0 (2D), σ = 1.5 (3D)
• Captures multi-scale spatial variation
Self-Adaptive Weights
• λᵢ = softplus(wᵢ) — always positive
• L = λ_pde·L_pde + λ_bc·L_bc + λ_end·L_end
• wᵢ learned jointly with network
• η_model = 1e-3, η_λ = 1e-4
• Balances PDE vs. boundary residuals
NAS Search Space
• Layers: 2 to 6
• Neurons per layer: 16 to 256
• Activations: tanh, swish, relu
• Skip connections: yes/no
• Fourier σ: 0.5 to 3.0
IC-consistent output: θ̂(x,τ)=θ_ic(x)+τ·Nθ guarantees exact satisfaction of initial conditions at τ=0

## Slide 7
Neural Architecture Search
Bayesian (TPE) vs. NSGA-II vs. NSGA-III
Neural Architecture Search
Bayesian (TPE)
• Tree Parzen Estimator
• Probabilistic surrogate model
• 800 training epochs
• Efficient single-objective
• Best FEM call reduction
• Fast convergence
NSGA-II
• Non-dominated Sorting GA
• 2-objective (L2, runtime)
• NAS: 800 ep, retrain: 1500 ep
• Pareto front exploration
• Crowding distance diversity
• Often best accuracy
NSGA-III
• Reference-point based EA
• Many-objective variant
• NAS: 800 ep, retrain: 1500 ep
• Structured reference points
• Better coverage of front
• Best 2D L2: 0.83%
Comparison Summary
Optimizer
Epochs (NAS)
Epochs (Retrain)
Strength
Best FEM Red.
Bayesian
800
—
Speed & consistency
5.0×
NSGA-II
800
1500
Accuracy on complex geom
1.0× – 2.0×
NSGA-III
800
1500
Best 2D (0.83% L-shape)
1.0× – 3.0×
All three optimisers search the same PINN architecture space; Bayesian best for FEM reduction, NSGA-III best raw L2

## Slide 8
2D Results — k-Skip Analysis
L2 relative error vs. k-skip factor (800 ep (NAS))
2D Results — k-Skip Analysis
800 Epochs (NAS phase)
800 ep (k-skip analysis)
Best 2D: L-shape NSGA-III k=1, L2=0.83%. Circle Bayesian k=3 gives 0.94% with 2.9× fewer FEM calls

## Slide 9
2D Heatmap — Rectangle (Bayesian, k=1)
Rectangle | Bayesian (TPE) | k=1 | L2=2.13% | MAE=2.1°C | Runtime=206 s
FEM reference (left) · PINN prediction (centre) · Absolute error (right)

## Slide 10
2D Heatmap — Circle (Bayesian, k=3)
Circle | Bayesian (TPE) | k=3 | L2=0.94% | MAE=2.0°C | FEM calls↓ 2.9×
FEM reference (left) · PINN prediction (centre) · Absolute error (right)

## Slide 11
2D Heatmap — L-shape (Bayesian, k=2)
L-shape | Bayesian (TPE) | k=2 | L2=0.94% | MAE=1.6°C | FEM calls↓ 2.0×
FEM reference (left) · PINN prediction (centre) · Absolute error (right)

## Slide 12
2D Summary Table
Best-k results per domain and optimizer (800 ep (NAS))
2D Summary Table
Best 2D: L-shape NSGA-III k=1, L2=0.83% | Bayesian Circle k=3: L2=0.94%, 2.9× FEM reduction | Most 2D results < 3% L2 error
Bayesian achieves best FEM reduction; NSGA-III achieves best raw L2 accuracy in 2D

## Slide 13
3D Results — k-Skip Analysis
L2 relative error vs. k-skip factor (800 ep (NAS))
3D Results — k-Skip Analysis
800 Epochs (NAS phase)
800 ep (k-skip analysis)
Best 3D: L-shape NSGA-III k=1, L2=0.91%. Bayesian Rectangular k=5: L2=4.12% with 5× fewer FEM calls

## Slide 14
3D Heatmap — Rectangular (Bayesian, k=5)
Rectangular | Bayesian (TPE) | k=5 | L2=4.12% | MAE=8.6°C | FEM calls↓ 5.0×
FEM reference (left) · PINN prediction (centre) · Absolute error (right)

## Slide 15
3D Heatmap — Cylinder (Bayesian, k=2)
Cylinder | Bayesian (TPE) | k=2 | L2=2.86% | MAE=5.0°C | FEM calls↓ 2.0×
FEM reference (left) · PINN prediction (centre) · Absolute error (right)

## Slide 16
3D Heatmap — Stacked (Bayesian, k=5)
Stacked | Bayesian (TPE) | k=5 | L2=4.03% | MAE=7.9°C | FEM calls↓ 5.0×
FEM reference (left) · PINN prediction (centre) · Absolute error (right)

## Slide 17
3D Heatmap — L-shape 3D (Bayesian, k=3)
L-shape 3D | Bayesian (TPE) | k=3 | L2=2.14% | MAE=5.1°C | FEM calls↓ 2.9×
3D problems show higher errors due to additional spatial dimension · L-shape NSGA-III k=1 achieves L2=0.91%

## Slide 18
3D Summary Table
Best-k results per domain and optimizer (800 ep (NAS))
3D Summary Table
Best 3D: L-shape NSGA-III k=1, L2=0.91% | Worst: Stacked NSGA-III k=3, L2=6.27% | Bayesian Rectangular k=5: 5.0× FEM reduction
3D geometry complexity impacts accuracy — Stacked geometry most challenging; L-shape unexpectedly best

## Slide 19
Before vs. After Retrain
Full summary comparison: 800 ep (NAS) vs 1500 ep (retrained)
Before vs. After Retrain
2D — Full Summary (Both Epochs)
3D — Full Summary (Both Epochs)
1500-ep retrain generally improves or stabilises accuracy vs. initial 800-ep NAS phase

## Slide 20
Warm-Start PINN Training
Carrying weights across windows — speed vs accuracy trade-off
• Strategy: Window 1 trains cold (800 ep, lr=1e-3); subsequent windows fine-tune from previous weights (500 ep, lr=1e-3)
• FEM still provides θ_ic at every window boundary — baseline unchanged
• Motivation: adjacent windows share similar physics; warm weights need fewer steps to adapt
• 3 variants tested: ws (300 ep, lr=3e-4), ws_500ep, ws_1000ep, ws_2000ep
Key Findings
• Bayesian: 1.5× speedup, ΔMAE ≈ +0.3°C ← ideal
• NSGA-II / III (2D): ~3× speedup, ΔMAE ≈ +1–2°C ← acceptable
• NSGA-II / III (3D): ~3× speedup, ΔMAE ≈ +5–9°C ← not recommended
• Anomaly: lshape 3D / nsga2 / k=5 — warm-start 12.5°C better than cold (cold-start failed to converge for that combination)
• Beyond 1000 warm epochs, time advantage is lost with no accuracy recovery
Rectangle / NSGA-II / k=3 (example)
Variant
Mean MAE
Runtime
Speedup
Cold (800 ep)
5.34°C
127 s
1.0×
Warm 300 ep
12.22°C
31 s
4.1×
Warm 500 ep
5.99°C
46 s
2.8×
Warm 1000 ep
5.81°C
76 s
1.7×
Warm 2000 ep
5.54°C
141 s
0.9×
★ ws_500ep: best accuracy/speed balance

## Slide 21
Warm-Start: MAE vs k (Cold / v2 / Warm)
Mean MAE across domains — cold-start (800 ep) vs v2 (Fourier+SA) vs warm-start (500 ep)
2D Domains
3D Domains
Bayesian v2 (Fourier+SA): consistent improvement over cold. Warm-start (500 ep) matches or exceeds cold (800 ep) at 38% fewer epochs.

## Slide 22
Warm-Start: Summary & Recommendation
Numeric summary table and colour-coded recommendation per (arch, domain)
Summary Table (2D)
Recommendation Matrix (2D)
Green = warm-start recommended | Yellow = marginal | Red = cold-start preferred.

## Slide 23
Warm-Start Heatmap — Rectangle 2D (Bayesian)
Bayesian | k=1 | Row1=Reference Row2=Cold(800ep) Row3=Warm(500ep) Row4/5=Error
Cold = 800 ep | Warm = 500 ep, lr=1e-3 | Lower error = better

## Slide 24
Warm-Start Heatmap — Rectangle 2D (NSGA-II)
NSGA-II | k=1 | Row1=Reference Row2=Cold Row3=Warm Row4/5=|Error|
Cold = 800 ep | Warm = 500 ep, lr=1e-3 | Lower error = better

## Slide 25
Warm-Start Heatmap — Rectangle 2D (NSGA-III)
NSGA-III | k=1 | Row1=Reference Row2=Cold Row3=Warm Row4/5=|Error|
Cold = 800 ep | Warm = 500 ep, lr=1e-3 | Lower error = better

## Slide 26
Conclusions & References
✔ 2D performance: most L2 < 3%; best = 0.83% (L-shape, NSGA-III, k=1)
✔ 3D performance: most L2 < 6%; best = 0.91% (L-shape 3D, NSGA-III, k=1)
✔ FEM call reduction: up to 5× with Bayesian on Rectangular and Stacked 3D
✔ Bayesian: fastest convergence, best FEM reduction with acceptable accuracy
✔ NSGA-II / III: higher accuracy but more FEM calls; best suited for precision tasks
✔ IC-consistent output + Fourier features + SA weights: robust across all geometries
✔ 1500-ep retrain (NSGA-II/III) improves absolute accuracy by ~0.2–0.5% L2
References
[1] Mortensen D., Noorsumar G., Fjær H.G., Babaei R., Drønen P.E. (2026). Modelling of distortions on large aluminium automotive subframes during casting, heat treatment and quenching. Int. J. Adv. Manuf. Technol. https://doi.org/10.1007/s00170-026-17515-w [2] Wang & Zhong (2023). NAS-PINN: Neural Architecture Search-guided PINN. arXiv:2305.10127