## Slide 1
NAS-PINNs
Neural Architecture Search for Physics-Informed Neural Networks
A356 Aluminum Water Quenching · FEM Skip Operator · Multi-Domain Poisson
L1 Single-Shot
L2 Skip Op.
L3 Hybrid FEM
L4 Distortion
L5 L-BFGS
L6 Poisson
L7 Multi-Dom.
2026

## Slide 2
Project Overview
Seven-level NAS-PINN framework for thermal simulation
NAS-PINNs Thesis | 2026
L1
Single-Shot PINN
Global T(t,x,y) over full time domain
L2
Skip Operator
FEM at anchors, PINN fills skipped steps
L3
Hybrid FEM+PINN
Adaptive residual-driven FEM/PINN routing
L4
Distortion Mechanics
Plane-stress thermal distortion at CMM pts
L5
L-BFGS Refinement
Second-order polish after Adam
L6
Poisson Benchmark
Generalization to Poisson PDE
L7
Multi-Domain
5 geometries: square, circle, annulus…
Core Thesis: PINN with NAS-optimized architecture can replace sequential FEM steps — solving in fewer solver calls without accuracy loss.

## Slide 3
Problem Statement
A356 Aluminum Water Quenching — Why PINNs?
NAS-PINNs Thesis | 2026
Physical Setup
▸ Part: A356 aluminum (1.3 × 0.6 m), T₀ = 540°C
▸ Process: immersed in water bath at T_w = 20°C
▸ Physics: ρCp·∂T/∂t = K·∇²T with Robin BC
▸ HTC: nonlinear h(T) — nucleate/film boiling regimes
▸ Goal: predict T(x,y,t) and distortion at 47 CMM points
FEM Bottleneck:
▸ Must solve 20 sequential time steps (t=1.5s each)
▸ Each step recomputes full mesh → expensive
▸ PINN opportunity: skip intermediate steps
Key Numbers
540°C → 20°C
Temperature range
30 seconds
Total quenching time
20 FEM steps
Sequential solves
3 NAS methods
Bayesian · NSGA-II · NSGA-III
7 Levels
Progressive framework
5 Geometries
Level 7B multi-domain

## Slide 4
Level 1 — Single-Shot NAS-PINN
Architecture search for global T(t,x,y) predictor
L1
NAS-PINNs Thesis | 2026
▸ NAS search space: layers ∈ {2..6}, neurons ∈ {32..256}, act ∈ {tanh, relu, swish}
▸ Three optimizers: Bayesian (TPE) · NSGA-II · NSGA-III
▸ Training: Adam 5000 ep, cosine LR: 1e-3 → 1e-5
▸ Reference: analytical T(t) = 20 + 520·exp(−1.75×10⁻³·t)
Optimizer
Architecture
L2_rel↓
MAE (°C)↓
NAS time
Bayesian ★
5×151 relu
0.076
39.1°C
~180s
NSGA-II
3×153 tanh
0.252
132.6°C
~120s
NSGA-III
3×75 tanh
0.513
270.3°C
~110s
Target
—
< 0.100
< 50°C
—
★ Only Bayesian meets the L2 < 0.10 target at Level 1

## Slide 5
Level 2 — Temporal Skip Operator
PINN learns T_n → T_{n+k}: FEM at anchors, PINN fills the rest
L2
NAS-PINNs Thesis | 2026
▸ FEM: 20 mandatory sequential steps (t = 0, 1.5, 3, … 30 s)
▸ Skip=k: FEM only at t[::k], PINN predicts skipped steps
▸ Window PINN: input [x, y, t_local, T_prev] → T_next
▸ IC teacher forcing: T_prev anchors each window
▸ Convergence: MAE ratio < 1.5× skip=1 baseline
Skip
FEM Steps
Bayesian
NSGA-II
NSGA-III
skip=1
21/21
43.6°C ✓
38.1°C ✓
44.4°C ✓
skip=2
11/21
33.2°C ✓
56.0°C ✗
75.0°C ✗
skip=4
6/21
57.5°C ✓
154.8°C ✗
202.1°C ✗
skip=6
4/21
93.6°C ✗
354.6°C ✗
428.6°C ✗
Key result: Only Bayesian NAS achieves skip=2 (2× FEM reduction) with convergence

## Slide 6
Level 3 — Hybrid FEM + PINN
Adaptive residual-driven routing: when to use FEM vs PINN
L3
NAS-PINNs Thesis | 2026
▸ PDE residual r(t) computed after each step
▸ r > threshold → FEM (high uncertainty)
▸ r ≤ threshold → PINN (safe to skip)
▸ Threshold = 0.1, max_skip = 4
Results:
▸ All 3 optimizers: 80% skip rate achieved
▸ Only 4–6 FEM steps out of 20
▸ Bayesian MAE maintained < 50°C
Adaptive Skip Logic
1
Solve step with current model
2
Compute PDE residual r(t)
3
r > 0.1 ?
3a
YES → Full FEM solve
3b
NO → PINN prediction only
4
Advance to t+1
Outcome: 80% FEM skip across all optimizers → Hybrid approach generalizes even for NSGA-II/III

## Slide 7
Level 4 — Thermal Distortion Mechanics
From PINN temperature field to CMM-point distortion
L4
NAS-PINNs Thesis | 2026
▸ Input: T(x,y,t=30s) from Level 3 PINN
▸ Plane-stress FEM: σ = E·α·ΔT
▸ Output: δ (mm) at 47 CMM measurement points
▸ Reference: paper Fig 17/18 measured distortion
Distortion Results (mean |δ|):
▸ Bayesian: 1.67 mm
▸ NSGA-II: 2.81 mm
▸ NSGA-III: 4.74 mm
Note: Bayesian thermal accuracy (L2=0.076) → lowest distortion
Direct correlation: better PINN → better distortion prediction
Mean Distortion |δ| (mm)
1.67 mm
Bayesian 5×151 relu
2.81 mm
NSGA-II 3×153 tanh
4.74 mm
NSGA-III 3×75 tanh

## Slide 8
Level 5 — L-BFGS Refinement
Second-order optimizer applied after Adam convergence
L5
NAS-PINNs Thesis | 2026
▸ Motivation: Adam converges to region, L-BFGS fine-tunes precisely
▸ L-BFGS: quasi-Newton, uses curvature information
▸ Strong Wolfe line search | max_iter = 500
▸ Applied to Level 1 Bayesian, NSGA-II, NSGA-III models
Optimizer
Adam L2
Adam MAE
L-BFGS L2
L-BFGS MAE
Improvement
Bayesian 5×151
0.076
39.1°C
0.030
14.4°C
2.6×↓
NSGA-II 3×153
0.252
132.6°C
0.055
28.7°C
4.5×↓
NSGA-III 3×75
0.513
270.3°C
0.259
136.4°C
2.0×↓
Target
—
—
< 0.100
< 50°C
—
L-BFGS brings all three optimizers closer to target: Bayesian L2: 0.076 → 0.030 ✓ | NSGA-II L2: 0.252 → 0.055 ✓ | NSGA-III: 0.513 → 0.259
Note: L-BFGS per-window for Level 2 time-stepper is LESS effective — window training needs sufficient Adam pre-convergence first.

## Slide 9
Level 6 — Poisson PDE Benchmark
Generalization test: does NAS-PINN work beyond heat equation?
L6
NAS-PINNs Thesis | 2026
▸ PDE: −∇²u = f(x,y) on unit square [0,1]²
▸ Exact solution: u = sin(πx)·sin(πy)
▸ Same NAS architectures from Level 1
▸ Auxiliary loss: boundary residual + PDE residual
Results:
▸ Bayesian: L2 = 0.0083 ✓ (best)
▸ NSGA-II: L2 = 0.0412 ✓
▸ NSGA-III: L2 = 0.1890 ✗ (marginal)
Key finding: NAS-optimized architectures generalize to different PDE families without re-search.
Bayesian NAS architecture (5×151 relu) achieves L2 = 0.0083 on Poisson PDE — demonstrates cross-PDE transferability without any architecture modification.

## Slide 10
Level 7 — Multi-Domain & Temporal Skip Analysis
7A: time-skip on quenching | 7B: 5-geometry Poisson NAS
L7
NAS-PINNs Thesis | 2026
Level 7A — Temporal Skip (Quenching)
▸ Bayesian: skip=4 still converges (L2 = 0.090)
▸ NSGA-II: skip=2 marginal (ratio 1.47×)
▸ NSGA-III: skip=2 diverges (ratio 1.76×)
▸ Skip efficiency: 80% FEM step reduction for Bayesian
Level 7B — Multi-Domain Poisson (5 Geometries)
▸ Domains: Square · Circle · Annulus · L-shape · Flower
▸ NAS optimized per geometry
▸ All converge: L2 < 0.05 for Bayesian
▸ NSGA-III struggles on complex geometries (flower)

## Slide 11
Cross-Level Comparison
All optimizers · All levels · Unified view
NAS-PINNs Thesis | 2026
Bayesian NAS
Best across all levels — only optimizer meeting ALL targets
NSGA-II
L-BFGS closes gap (L2: 0.252→0.055) but skip=2 needs 5000+ epochs
NSGA-III
Smallest model (11k params) — limited skip capability

## Slide 12
Conclusions & Key Findings
✓
PINN can replace FEM steps without accuracy loss
Bayesian skip=2 (11/21 FEM steps): MAE = 33.2°C vs 43.6°C baseline
✓
NAS architecture matters for skip capability
Bayesian 5×151 relu converges; NSGA-II/III (smaller) diverge at skip=2
✓
L-BFGS refinement significantly improves all optimizers
Bayesian L2: 0.076→0.030 | NSGA-II L2: 0.252→0.055 (4.5× improvement)
✓
Hybrid FEM+PINN achieves 80% step reduction
Adaptive residual routing works for all 3 optimizers
✓
NAS architectures generalize across PDE families
Same architecture: heat equation → Poisson PDE, 5 geometries
→
Future: NSGA-II skip=2 with 5000 epoch training
Current 500-epoch result ratio=1.47× — just above 1.5× threshold
NAS-PINNs: Temporal Skip Operator for FEM Acceleration | 2026